## Slide 1: RBE550 Motion Planning OMPL Overview
Constantinos Chamzas www.cchamzas.com www.elpislab.org

## Slide 2: Disclaimer and Acknowledgments
The slides are a compilation of work based on notes and slides mainly from Zak Kingston, , but also Ali Golestaneh

## Slide 3: Overview
OMPL at High Level
OMPL Internals

## Slide 4
OMPL at High Level

## Slide 5: What is OMPL?
OMPL is a C++11 Library (with automatically generated Python Bindings), intended for industrial, educational, and academic use, which has:
Core data-structures for sampling-based planners
Commonly used heuristics, components, etc.
Implementation of many state-of-the-art sampling-based planners
  With details of many low-level details skipped in their corresponding papers!

## Slide 6: What is OMPL not?
OMPL does not:
• Represent robot and scene geometry
• Compute forward and inverse kinematics
• Provide collision checking routines
• Simulate robot dynamics
• etc.
OMPL is an abstract library that you must provide the guts for!

## Slide 7: What is OMPL.app?
OMPL.app is a lightweight GUI front-end to OMPL that uses a triangle mesh representation of free-flying robots in an environment

## Slide 8
OMPL Internals

## Slide 9: Sampling-Based Planners
Figure 2: A Simple Graph-based Sampling-based Planner

## Slide 10: OMPL is an Abstract Interface
OMPL requires you to define all the components of a motion planning problem:
State Space e.g., the configuration space
State Validator e.g., a collision checker
State Sampler e.g., a uniform sampler
Start & Goal e.g., start and goal states
Motion Planner Pick your favorite!
And so on...
These are specific to your robot and environment, your motion planner, and your problem!

## Slide 11: OMPL is an Abstract Interface
OMPL requires you to define all the components of a motion planning problem:
State Space e.g., the configuration space
State Validator e.g., a collision checker
State Sampler e.g., a uniform sampler
Start & Goal e.g., start and goal states
Motion Planner Pick your favorite!
And so on...
These are specific to your robot and environment, your motion planner, and your problem!

## Slide 12: States & State Spaces

## Slide 13: States & State Spaces

## Slide 14: OMPL is an Abstract Interface
OMPL requires you to define all the components of a motion planning problem:
State Space e.g., the configuration space
State Validator e.g., a collision checker
State Sampler e.g., a uniform sampler
Start & Goal e.g., start and goal states
Motion Planner Pick your favorite!
And so on...
These are specific to your robot and environment, your motion planner, and your problem!

## Slide 15: State Validators
The state validator is problem specific, and must be defined by the user / layer on OMPL.
• e.g., OMPL.app, MoveIt!, V-REP, and the list goes on...
For a robot, this could be a collision checker, are joint angles in bounds, etc.
For a molecule, this could be the energy of the state, use the metropolis criterion, etc.
Optionally, state validators can return:
• Distance to nearest invalid state (i.e., obstacle)
• Gradient of distance
Which planners and other components can use!

## Slide 16: Collision Checking
• ROS (robot operating system, common middleware used in robotics) offers a sensor-driven world model with point clouds (represented as octrees) and
triangle meshes.
• OMPL.app uses triangle meshes and FCL (flexible collision library) for collision checking.
• Easy to add wrappers to whatever collision checker you want!
To do collision checking, you must first choose a model of the world (e.g., point clouds, triangle meshes, etc.)
Images from pointclouds.org and PQP site

## Slide 17: OMPL is an Abstract Interface
OMPL requires you to define all the components of a motion planning problem:
State Space e.g., the configuration space
State Validator e.g., a collision checker
State Sampler e.g., a uniform sampler
Start & Goal e.g., start and goal states
Motion Planner Pick your favorite!
And so on...
These are specific to your robot and environment, your motion planner, and your problem!

## Slide 18: State Samplers
Every State Space needs a State Sampler
• Sample Uniformly
• Sample Nearby
• Sample from a Gaussian
These can be specialized (i.e., biased), e.g., bridge test, experience-based, medial axis, etc.

## Slide 19: How to Sample Uniformly in Different Spaces?
How do you uniformly sample inside the area of a circle, and more generally a ball in ?

## Slide 20: How to Sample Uniformly in Different Spaces?
Right:
Wrong:

## Slide 21: Marsaglia n-Ball Sampling
Marsaglia, G. ”Choosing a Point from the Surface of a Sphere.” Ann. Math. Stat. 43, 645-646, 1972.

## Slide 22: So Many Ways to Get Sampling Wrong
Right:
Wrong:
e.g., 3D Rotations:

## Slide 23: Nearest Neighbors
A nearest neighbor datastructure (NN) is essential for most sampling-based planners. NNs allow for efficient lookup of spatial similar points.
k-NN (the k nearest neighbors to a point) can be computed efficiently with kd-trees in low-dimensional, Euclidean (Rn) spaces.
In high-dimensional spaces, approximate NN works much better.
In non-Euclidean spaces (e.g., any space with rotations), data structures other than kd-trees are necessary. OMPL provides a few implementations (GNATs for metric spaces, etc.).

## Slide 24: Valid State Samplers
Valid State Samplers combine State Samplers with Validity Checkers.
In the simplest form: sample n times until the state is valid.
Can try other strategies, like finding states with high clearance or in narrow regions.

## Slide 25: OMPL is an Abstract Interface
OMPL requires you to define all the components of a motion planning problem:
State Space e.g., the configuration space
State Validator e.g., a collision checker
State Sampler e.g., a uniform sampler
Start & Goal e.g., start and goal states
Motion Planner Pick your favorite!
And so on...
These are specific to your robot and environment, your motion planner, and your problem!

## Slide 26: Goals

## Slide 27: OMPL is an Abstract Interface
OMPL requires you to define all the components of a motion planning problem:
State Space e.g., the configuration space
State Validator e.g., a collision checker
State Sampler e.g., a uniform sampler
Start & Goal e.g., start and goal states
Motion Planner Pick your favorite!
And so on...
These are specific to your robot and environment, your motion planner, and your problem!

## Slide 28: Planners
Planners take in as input Problem Definitions. Problem definitions have at least one start state and a goal object.
Planners only need to implement two methods:
• solve: Takes a Planner Termination Condition as an argument. This can be based on time, external events, etc.
• clear: Clear internal memory, get ready to solve another problem

## Slide 29: Many Planners Available in OMPL

## Slide 30: The OMPL Bifurcation
There are two main namespaces in OMPL:
• geometric: Planning for rigid bodies with geometric constraints (e.g., manipulators, free-flying bodies, in general holonomic robots). This will be Project 3.
• control: Planning for systems with dynamical constraints (e.g., cars, torque controlled manipulators, generally non-holonomic robots). This will be Project 4.

## Slide 31: Control Spaces

## Slide 32
Summing Up…

## Slide 33: API Overview

## Slide 34: Planner Arena (http://plannerarena.org)

## Slide 35: OMPL Online
Website at http://ompl.kavrakilab.org/, with:
• Searchable documentation
• Tutorials
• Demos
• and More!

## Slide 36
Live Demo!